## Slide 1: Rocket Avionics
2/14/2012
Aaron Mitchell

## Slide 2: What are Rocket Avionics?
Regular Avionics
  Anything electronic on a…
    Aircraft
    Missile
    Satellite/spacecraft
  Including…
    Navigation
    Piloting
    Communication
    Monitoring
    Intelligence
Our Avionics
  Rocket recovery systems

## Slide 3: Rocket Avionics: Goals
Primary Goal: RECOVERY!
  To deploy the parachute needs:
    Method of deployment
    Know when to deploy
Secondary Goals
  Data Collection
  Radio Beacons
  Telemetry
  GPS location
  Extra Intelligence
YES!!!

## Slide 4: Recovery
Simply Difficult.

## Slide 5: Parachute Go Forth!
Parachute deployment
  Black powder charges
  Compressed neutral gas
  Pneumatic piston
All triggered by electronics
  Almost always using
  the all-powerful…..
  …..E-Match!
  Special resistor ignites when
  given correct current.

## Slide 6: Altimeter
Keep track of altitude
Bonus: Detonate charges
We used to use ARTS board
  2 Pyro Channels
  $180
Now use Featherweight Raven
  4 Pyro Channels
  $155
  ¼ the size!

## Slide 7: Raven
Programming Interface Included
  Used to Program 4 Pyro Channels
Includes:
  Single-Axis Accelerometer
  Barometer
  Timer
  Bunch of safety features (elementary-school level intelligence)

## Slide 8: Intelligence and Decision Making
Can you say Microcontrollers!

## Slide 9: Microcontroller
Programmable mini-computer
  Hobby models include ports to easily read/write voltage signals
  Analog, digital, or both!
Lots out there
  Many different languages
  Many different applications
  Not all user friendly!
Which one do we use?...

## Slide 10: Arduino!
Arduino = MatLAB of microcontrollers
  Has it’s own language
  Support community
  Free code development kit
  Lot of FREE help with code
Very versatile!
  Balance of easy coding and capability

## Slide 11: Programming
Brains?

## Slide 12: Programming?
Just kidding. (sample arduino code – normal persons face)

## Slide 13: Telemetry and GPS
Marco…

## Slide 14: Telemetry
Why is it not easy?
  Transmitting signals is not easy when:
    Supersonic
    Vibrating like crazy
    Temperature fluctuations
    Made of carbon fiber (not RF transparent)
  PLUS. We have to receive those signals
    Means investing in expensive ground station equipment
    HAM radio licenses
    Transmitter not easily tracked
    Loss of line of sight on the way down

## Slide 15: GPS
Important attributes
  Power (aka range)
  Antenna (satellite antenna)
  Acquisition Time
  Programmability
  Lock-out (civilian models only)
Lock out occurs at either
  18 km altitude (11 mi)
  515 m/s (1152 mph, ~1.5 Mach)
  Both, varies by manufacturer

## Slide 16: Our System
Definitely Experts

## Slide 17: Early Planning

## Slide 18: Arduino System
Pressure transducer, transmitter, proto board, Garmin GPS, Arduino MEGA. Transmits on 900 MHz frequency.

## Slide 19: Big Red Bee GPS System
Most powerful system, transmits on 2m band.

## Slide 20: Byonics GPS System
Also transmits on 2m band, just less frequently. Redundant system designed to last days.

## Slide 21: Ground Systems
900 MHz Dish Antenna, 2m Dipole Antenna

## Slide 22: Pop Quiz Review: WTF is this??